## Slide 1: Programming on Embedded Circuits

## Slide 2: Micro-Controller Platform
Micro-Controller Unit (MCU) contains RAM, ROM and IO
Micro-Processor Unit (MPU) only contains the CPU
System on Chip (SoC) refers to MCUs with a greater number of onboard peripherals and functionality
http://www.microchip.com
http://www.ti.com
http://theairboard.cc

## Slide 3: C Language: Header and C++ Files
#ifndef __LED_H_
#define __LED_H_
#include <system_lib.h>
#include “user_lib.h”
#include “UserFolder/lib.h”
extern int T_on;
extern int T_off;
void setOn(long duration);
void setoff(long duration);
#endif
#include “led.h”
int T_on;
int T_off;
int counter;
void setOn(long duration){
//TODO: set LED on here
}
void setoff(long duration){
//TODO: set LED off here
}
void delay(long duration){
//TODO: set delay here
}

## Slide 4: C Language: Main File
#include “led.h”
#include “timer.h”
#include “gpio.h”
#include “button.h”
void main(){
initGPIO();
initTimer();
initButton();
initLED();
….
….
while(1){};
}
void timer_isr(){
}
void ext_isr(){
}
LED
TIMER
GPIO
BUTTON
System operations are implemented in interrupt functions
Modules/ Libraries are included
Modules/ Libraries are initiated

## Slide 5: Finite State Machine (FSM)
Finite-State Machine (FSM) or Deterministic Finite Automata (DFA), finite automaton, or simply a state machine, is a mathematical model of computation
A turnstile
Current State | Input | Next State
Locked | Coin | Unlocked
 | Push | Locked
Unlocked | Coin | Unlocked
 | Push | Locked

## Slide 6: Finite State Machine Programming
while(1){
  switch(status){
    case LOCKED: lock_turnstile(); //operation in a state
    if(Coin == true) //transition condition
    status = UNLOCKED; //next state
    break;
    case UNLOCKED:
    unlock_turnstile(); //operation in a state
    if(Push == true) //transition condition
    status = LOCKED; //next state
    break;
    default:
    break;
    }
}

## Slide 7: Example 1
Given an LED turns on for T_on and then turns off for T_off.
  Design an DFA for this LED
  Implement the DFA in Arduino
digitalWrite(13, HIGH): turn on the LED
digitalWrite(13, LOW): turn off the LED
setTime(duration): set a clock (timer_flag = 0), when the clock is expired, timer_flag = 1; duration is in mili-seconds.

## Slide 8: Answer
INIT: Set pin 13 to OUTPUT mode, set timer
LED_ON: Turn on the LED
LED_OFF: Turn off the LED
INIT
LED_ON
LED_OFF
timer_flag == 1
timer_flag == 1

## Slide 9: Answer (Arduino Code)
void loop(){
  switch(status){
    case INIT: pinMode(13, OUTPUT);
    setTimer(T_on);
    status = LED_ON;
    digitalWrite(13, HIGH);
    break;
    case LED_ON:
    if(timer_flag == 1){
  status = LED_OFF;
  setTimer(T_off);
  digitalWrite(13, LOW);
    }
    break;
    case LED_OFF:
    if(timer_flag == 1){
  status = LED_ON;
  setTimer(T_on);
  digitalWrite(13, HIGH);
    }
    break;
    default:
    break;
    }
delay(10);
}
void timer_run(){
if(timer_counter > 0)
timer_counter--;
if(counter_timer == 0)
timer_flag =1;
}
void setTimer(long duration){
timer_counter = duration;
timer_flag = 0;
}

## Slide 10: Example 2
Design a smart lock which accepts 4 digits as a secrete code. However, there is a time-out for each digit (e.g. T_out = 5s). After this period, the system is reset

## Slide 11: Embedded Platform based on Operating System
Embedded means something that is attached to another thing.
“Any sort of device which includes a programmable computer but itself is not intended to be a general-purpose computer” [Marilyn Wolf]
Embedded system has three components:
  Hardware
  Real Time Operating System (RTOS)
  Software

## Slide 12: Classification of Embedded System
Small Scale
Medium Scale
Sophisticated Scale

## Slide 13: Processor
Processor is the heart of the Embedded Syste
General Purpose processor (GPP)
  Microprocessor
  Microcontroller
  Embedded Processor
  Digital Signal Processor
Application Specific System Processor (ASSP)
Multi Processor System using GPPs

## Slide 14: Operating System: Linux and Android
Connectivity and UI
  Two powerful operating systems used in most of the embedded systems
  Wireless connectivity and graphics interface: Android OS
  Linux comes with a complex flow and it might be difficult for a beginner to understand it
Power management
  Android and Linux supports effective power management compared to real time operating systems
Responsiveness
Cost

## Slide 15: Android Operating System Component

## Slide 16: Android Boot File
mkdir /system
mkdir /data 0771 system system
mkdir /cache 0770 system cache
mkdir /config 0500 root root
mkdir /metadata 0770 root root
service yunos_preinstall /system/bin/yunos_preinstall.sh
user root
group root
class main
disabled
oneshot

## Slide 17: Android Resource File
IR Remote Data

## Slide 18: Android System File
System apps
User apps
Launcher apps
Preinstall apps
Libs
KeyLayout
…

## Slide 19: How to Port Android Things?

## Slide 20: Create an Android Things Project
http://developer.android.com/things/training/first-device/create-studio-project
Prerequisites
  Update your SDK tools to version 25.0.3 or higher The updated SDK tools enable you to build and test apps for Things.
  Update your SDK with Android 8.1 (Oreo), API 27 or higher The updated platform version provides new APIs for Things apps.

## Slide 21: Create an Android Things Project
Added library
Home Activity
dependencies { ... compileOnly 'com.google.android.things:androidthings:+' }