## Slide 1: CO2015 Exercise – BJT

## Slide 2
When a transistor is used as a switch, it is stable in which two distinct regions?
  saturation and active
  active and cutoff
  saturation and cutoff
  none of the above
Notes: C

## Slide 3
For a silicon transistor, when a base-emitter junction is forward-biased, it has a nominal voltage drop of
  0.7
  0.3
  0.2
  VCC
Notes: A

## Slide 4
A certain BJT has IB = 167uA, IC = 15mA, the amplifier DC factor is:
  15
  167
  90
  All are not correct

## Slide 5
Refer to the given figure. The most probable cause of trouble, if any, from these voltage measurements is
Notes: Base and Emitter is opened

## Slide 6
Refer to the given figure. The most probable cause of trouble, if any, from these voltage measurements is
Notes: No problem

## Slide 7
Refer to this figure. If VCE = 0.2 V, IC(sat) is

## Slide 8
Refer to this figure. Determine the minimum value of IB that will produce saturation (VCE(sat) = 0.2V).
Notes: 10=4.7*10^3*Ic+0.2
Ic = 2.085 ma.
Ib = 2.085/200 = 10.425 uA .

## Slide 9
Refer to this figure. The value of VBC is
Notes: -9.2

## Slide 10: CO2015 Exercise – FET

## Slide 11
Refer to the given figure. Calculate the value of VDS

## Slide 12: Answer
2V
Notes: 20V = 2k * ID + VDS + 1K*ID
VDS = 20 – (2 + 1)*6 = 2V

## Slide 13
Refer to figure shown below. Determine the value of VS.
Notes: VS = RS * ID = 6V

## Slide 14: Answer
6V

## Slide 15
A self-biased n-channel JFET has a VD = 6 V. VGS = –3 V. Find the value of VDS.
  -3V
  -6V
  3V
  6V

## Slide 16: Answer
3V

## Slide 17
Refer to the given figure. ID = 6 mA. Calculate the value of VDS

## Slide 18
-9V
In general VDS= VDD-(ID*RD) But in figure direction of FET transistor is out of drain so, Id becomes negative .

## Slide 19
Refer to the given figure. ID = 6 mA. Calculate the value of VDS

## Slide 20: Answer
6V

## Slide 21
Refer to figure given below. Determine the value of VGS

## Slide 22: Answer
-6V

## Slide 23
Refer to figure show below. Calculate the value of VD

## Slide 24: Answer
8V

## Slide 25
For a JFET, the value of VDS at which ID becomes essentially constant is the
  pinch-off voltage.
  cutoff voltage.
  breakdown voltage.
  ohmic voltage.

## Slide 26: Answer: A

## Slide 27
The value of VGS that makes ID approximately zero is the
  Pinch-off voltage
  Cut-off voltage
  Breakdown voltage

## Slide 28: Answer
B

## Slide 29
The ________ has a physical channel between the drain and source.
  DFET
  EFET
  VFET

## Slide 30: Answer: A

## Slide 31
What type(s) of gate-to-source voltage(s) can a depletion MOSFET (D-MOSFET) operate with?
  Zero
  Positive
  Negative
  All of them

## Slide 32
Midpoint bias for a D-MOSFET is ID = ________, obtained by setting VGS = 0
  IDSS / 2
  IDSS / 3.4
  IDSS
Notes: C

## Slide 33
Identify D-FET p channel

## Slide 34: Answer
B

## Slide 35
Determine VGS and ID

## Slide 36: Answer
Determine the Load line
  ID = 0
  ID = IDSS
  Q is the intersection point of the load line & transfer curve.
    ID = 5.07 mA
    VGS = -2.3V

## Slide 37
Determine VGS and ID for the given JFET, where
  IDSS = 5mA and VGS(off) = -4V

## Slide 38: CO2015 Exercise – Op Amp

## Slide 39
Calculate the output gain of the circuit if R1 = 100(Ohm) and Rf = 1(KOhm)

## Slide 40: Answer
11

## Slide 41
Refer to the given figure. A dc input signal of –50 mV is applied. You would measure ________ from the inverting input to ground.
  50mV
  1.05V
  -1.05V
  -50mV

## Slide 42
Calculate the input voltage if the final output is 10.08 V
  0.168V